## Slide 1: Original Image: Gridded Cells
Provided by Ma Laboratory
  Worcester Polytechnic Institute
  Microfabricated slides with adhesive at gridded locations for cells to attach to.
Cells are encapsulated in a gel and lysed, DNA diffuses radially.
  Cells can be characterized by the nucleus and halo.
  Sometimes multiple cells attach to one location

## Slide 2: Thresholded Image (3 levels)
Use MATLAB function multithresh to separate image into nucleus, halo, and background segments.
  Combine halo and nucleus segments to get binary cell images.
  Use binary image to remove clustered cells.
  Use halo and nucleus to derive DNA damage.
  Use halo to detect apoptosis.

## Slide 3: Comparison of Measurements
Roundness metric
  Thresh: 0.820
Eccentricity metric
  Thresh: 0.500
Eccentricity is much better, as there is much more disparity between the single and multiple cell clusters
  Most single cells ~ 0.300
  Most multi cells ~ 0.650

## Slide 4: Choosing Thresholds and Regions for Calculation
When threshholds = 3, the measure of eccentricity is less disparate between cells that are manually determined to pass the criteria than those that do not vs using 2 thresholds, this is because we are using all thresholds together to make a binary image in order to do the calculation. The following are comparisons with 2, 3 thresholds for binary and nuclear comparisons. Note that if doing the nuclear way, matching has to be done early.
2B
3B

## Slide 5: Choosing Thresholds and Regions for Calculation
When threshholds = 3, the measure of eccentricity is less disparate between cells that are manually determined to pass the criteria than those that do not vs using 2 thresholds, this is because we are using all thresholds together to make a binary image in order to do the calculation. The following are comparisons with 2, 3 thresholds for binary and nuclear comparisons. Note that if doing the nuclear way, matching has to be done early.
2N
3N

## Slide 6: Matching Algorithm
Find matching nucleus and halo for each cell
Ignores when there are more of one than the other
  Happens when cell is too faint or multiple nuclei/cells in a bunch
Comparison of passing halo and nuclei structs individually or as part of a larger struct [insignificantly different, thus together is easier]
  Individually:
    Mean: 1.482 e-4
    Stdev: 3.3503 e-4
  Together:
    Mean: 1.0460 e-4
    Stdev: 3.0512 e-4

## Slide 7: DNA Damage Metrics
Cells

## Slide 8: DNA Damage time test
Want to know speed of DNA damage algorithms
Use speed calculations to determine algorithm O(f(n))
Test:
  Image resolution: 720 x 420 px
  Image size: 1,037,004 B
Results:
  The algorithm order is O(n)
Chart: Speed of DNA Damage Algorithm
| 10 | 20 | 30 | 40 | 50 | 60
Speed (s) | 1.214 | 2.124 | 3.035 | 3.915 | 4.913 | 5.731